## Slide 1: Medium Access Control in Data Link Layer
SMU, 휴먼지능정보공학과

## Slide 2: Contents
Data Link Layer Overview
Medium Access Control
  Brief Introduction to Wireless Medium
  Random Access
    ALOHA
    CSMA
    CSMA/CD
    CSMA/CA
  Controlled Access
  Channelized Access

## Slide 3: Data Link Layer
The data link layer provides a reliable (error-free) link
    Transfer data from the network layer of one machine to the network layer of another machine using hop by hop transmission over single links.
  Convert the raw bit stream of the physical layer into groups of bits (“frames”) and vice versa

## Slide 4: IP address & Data Link layer address
L2
L1
L8
L7

## Slide 5: Data Link Layer: Duties
Framing
Physical addressing
Flow control
Error control
Medium Access control
  determines how to share a link by many hosts
Logical Link Control sublayer

## Slide 6: Data Link Layer: Two sublayers
Data link layer can be divided into two functionality-oriented sublayers
IEEE made this division for Data Link Layer in LAN(Local Area Network)s
Medium Access Control (MAC) sublayer
Logical Link Control (LLC) sublayer

## Slide 7: Contents
Data Link Layer Overview
Medium Access Control
  Brief Introduction to Wireless Medium
  Random Access
    ALOHA
    CSMA
    CSMA/CD
    CSMA/CA
  Controlled Access
  Channelized Access

## Slide 8: Medium Access Control = Media Access Control = Multiple Access protocols

## Slide 9: Contents
Data Link Layer Overview
Medium Access Control
  Brief Introduction to Wireless Medium
  Random Access
    ALOHA
    CSMA
    CSMA/CD
    CSMA/CA
  Controlled Access
  Channelized Access

## Slide 10: Electromagnetic Spectrum for wireless

## Slide 11: Wireless Link Characteristics
Differences from wired link:
  decreased signal strength: radio signal attenuates as it propagates through matter (path loss)
  interference from other sources: standardized wireless network frequencies (e.g., 2.4 GHz) shared by other communication devices (e.g., phone); other devices (microwave oven, motors) interfere as well
  multipath propagation: radio signal reflects off objects ground, arriving ad destination at slightly different times
make communication across (even a point to point) wireless link much more “difficult”

## Slide 12: Wireless Signal Attenuation
Signal attenuates logarithmically with the distance
  Precv  Psend * (1/r)n
  r is the distance between sender and receiver
  n is the path loss exponent which is characteristic of the environment. Usually, between 2 in free space, to up to 6 indoors
To receive correctly, the received signal power should be high enough, compared to the noise level (Signal to Noise ratio, SNR)

## Slide 13: Effect of signal attenuation
Transmission range
  communication possible
  low error rate
Detection range
  detection of the signal possible
  no communication possible
Interference range
  signal may not be detected
  signal adds to the background noise
distance
sender
transmission
detection
interference
No effect

## Slide 14: Multiple node case
Multiple wireless senders and receivers create additional problems (beyond multiple access):
A
B
C
Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other
means A, C unaware of their interference at B
A
B
C
A’s signal
strength
space
C’s signal
strength
Signal fading (Another hidden terminal problem):
B, A hear each other
B, C hear each other
A, C can not hear each other interfering at B

## Slide 15: Contents
Data Link Layer Overview
Medium Access Control
  Brief Introduction to Wireless Medium
  Random Access
    ALOHA
    CSMA
    CSMA/CD
    CSMA/CA
  Controlled Access
  Channelized Access

## Slide 16: Random Access
Each station has the right to access the medium without being controlled by any other station
Collision, an access conflict, if more than one station tries to send
Multiple Access
Carrier Sense
Multiple Access
Collision Detection
Collision Avoidance

## Slide 17: ALOHA
The earliest random access method developed at the Univ. of Hawaii in the early 1970s
Designed for a radio (wireless) LAN
ALOHA and Slotted ALOHA
Frames in an ALOHA network:
How do we detect a collision?
When do we resend a collided frame?

## Slide 18: ALOHA Basic Assumptions
Station model - n independent stations each generating frames for transmission. One frame is generated and transmitted at a time per station.
Single channel - A single channel is shared with other stations.
Collision - Overlapping transmissions destroy the frames, can be detected later by some upper layer functions, and require retransmission. Collisions are the only errors.

## Slide 19: ALOHA protocol: Basics
When a station wants to transmit, it transmits
Collisions are detected at a higher layer of the receiving station.
  If no collision, an Acknowledgement (ACK) frame is sent back to the transmitting station.
  If collision, ACK will not be sent. The transmitting station will retransmit later.
Simple logic
Highly inefficient at large loads. Maximum utilization of 18% at a mean load of 0.5 transmission

## Slide 20: ALOHA Protocol: Retransmission Procedure
Binary exponential back-off algorithm

## Slide 21: Carrier Sense Multiple Access (CSMA)
What if we can sense whether medium is busy?
CSMA
  “Sense before transmit”
  “Listen before talk”
CSMA can reduce the possibility of collision, but it can not eliminate it because of propagation delay

## Slide 22: CSMA/CD
Senders can detect collision. How can we improve the efficiency?
CSMA with collision detection(CD):
  Listen while you are sending a packet (this is how you detect collision)
  Stop sending when collision happens
  Exponential back-off: Wait random time before you attempt to resend.
IEEE 802.3 standard, Ethernet

## Slide 23: Case in Wireless network
In wireless network, a sender cannot detect collision.
  Signal level is variable and is a function of distance.
  Sender’s transmission level can be much larger than a received signal level
How can we improve the efficiency of CSMA?
Three strategies
  When idle found, wait for some time and then randomly choose when to transmit: Inter frame space & Contention window
  Wait for ACK

## Slide 24: CSMA/CA (Collision Avoidance)
These strategies are called CSMA/CA collectively.
What if another station transmit during Contention window?
  We do not reset the back-off counter. We stops the timer and restarts it when the channel becomes idle
IFS may be used for priority control.

## Slide 25: CSMA/CA: Flow Diagram

## Slide 26: Contents
Data Link Layer Overview
Medium Access Control
  Brief Introduction to Wireless Medium
  Random Access
  Controlled Access
  Channelized Access

## Slide 27: Medium Access Protocols

## Slide 28: Controlled Access
The stations consult one another to find which station has the right to send
Reservation/Polling/ Token passing
Reservation access method:
  Each station makes a reservation in its own mini-slot.
  It needs a sophisticated synchronization: Less flexible.

## Slide 29: Polling: Select and Poll Functions
One primary and other secondary stations
How to exchanges data between A & B?
  Through primary station
Can a secondary station ask for transmission without poll?
  No

## Slide 30: Token Passing
With token passing, network is organized in a Logical Ring.
Special packet called a token circulates through the ring.
Token is the right to access the network.
Token should be managed e.g. from loss.
Physical topologies:
Hub is a multiport repeater
(Layer 1 device).

## Slide 31: Repeater & Hub
Repeater
  Operates at the Physical layer of the OSI model
  Has basic functions of
    Receiving signal, cleaning up
    Transmitting the signal on to the next link, bit by bit
  Extends the network beyond the maximum length of a single segment
  Connects segments of the same network (e.g. Ethernet), even if they use different media
Hub
  Multi-port repeater
Bridge & Switch
  Can perform basic CSMA/CD function of MAC layer
  “Layer 2” device

## Slide 32: Contents
Data Link Layer Overview
Medium Access Control
  Brief Introduction to Wireless Medium
  Random Access
  Controlled Access
  Channelized Access

## Slide 33: Medium Access Protocols

## Slide 34: FDMA
Available bandwidth of the common channel is divided into bands that are separated by guard bands
FDMA is an access method in data link layer protocol.
FDM is a physical layer technique that combines lower bandwidth channels into a higher bandwidth channel

## Slide 35: TDMA
The bandwidth is just one channel that is timeshared between different stations
Synch is needed, but maybe difficult because of propagation delay among stations.
  This problem should be covered with guard time.
TDMA is an access method. TDM is a physical layer technique that combines slower input channels into faster output channels.

## Slide 36: CDMA
One channel carries all transmissions simultaneously
Data from stations (d1, d2 , d3 , d4) are multiplied by codes (c1, c2, c3, c4) then sent.
Codes have two properties:
  If we multiply each code by another, we get 0. (e.g. c2· c3 = 0)
  If we multiply each code by itself, we get 4 (e.g. c2 · c2 = 4)
Data decoded by c1 = (d1.c1 + d2.c2 + d3.c3 + d4.c4) .c1
    = d1.c1.c1 + d2.c2.c1 + d3.c3.c1 + d4.c4.c1 = 4.d1

## Slide 37: CDMA: Encoding and Decoding
How four stations share the link during a 1-bit interval

## Slide 38: CDMA: Signal Level
Digital signal created by four stations in CDMA using NRZ-L for simplicity

## Slide 39: CDMA: Decoding
How station 3 can detect the data by station 2 by using the code for station 2
Decoding of the composite signal for one in CDMA